## Slide 1
CabinSense
In-Cabin Disturbance Intelligence
A real-time multi-modal AI platform that detects micro-distractions, fuses them into a Cognitive Load score, and delivers confirm-first cabin mitigations.
< 1 ms Fusion Latency
Fully Offline · No Cloud
SDV-Ready Architecture
Hackathon Build · 2 Days
github.com/PrashantKramadhari/in-cabin-hackthon

## Slide 2
THE PROBLEM
Drivers Face Continuous, Unmonitored Micro-Distractions
CRITICAL GAP
→ No infant / pet welfare monitoring
→ No object hazard detection
→ No cognitive load awareness
→ Cabin is the blind spot of modern ADAS
5 REAL SCENARIOS
→ Baby crying while driving (distraction)
→ Child / pet left behind (safety)
→ Unsecured objects before pothole (hazard)
→ Driver fatigue or stress (cognitive load)
→ Auto cabin changes without consent (UX)
OUR INSIGHT
→ These are NOT 5 products
→ They are 5 use cases on ONE pipeline
→ sense → detect → fuse → adapt
→ One scoring engine for all scenarios
→ Scoring on Innovation, Safety, Feasibility

## Slide 3
ARCHITECTURE
Edge-Node + Async Bus + Decision Engine
SENSING NODES
→ Radar (mmWave) — occupancy, HR, breathing
→ Microphone — BabyNet CNN + AST fallback
→ Camera — Qwen2-VL, MediaPipe, YOLOv8n
→ IMU / Vibration — road quality, pothole ahead
→ Vehicle CAN — speed, visibility, GPS
FUSION ENGINE (CORE)
Async Pub/Sub Bus
bus.py · bounded queue · <1ms latency
↓
World State
world.py · shared ground-truth cabin state
↓
Fusion + Decision
fusion.py · 10Hz · Cognitive Load → Mitigations
↓
WebSocket /ws
JSON state pushed to HMI at 10Hz
HMI / FEEDBACK
→ React Cabin HMI (zero-build)
→ Circular Cognitive Load gauge
→ Mitigation cards (Apply / Dismiss)
→ ANC / Volume / AC / Lighting
→ Confirm-First — nothing auto-acts
→
→
→
→
→
→
→
→

## Slide 4
FUSION ENGINE · CORE
Cognitive Load Score — Multi-Modal Weighted Accumulator
COGNITIVE LOAD FORMULA (fusion.py)
── Driver vitals (Radar micro-Doppler) ──────────────────────────
if HR > 95: CL += min(30, (HR−95) × 1.5)
if RESP > 20: CL += min(15, (RESP−20) × 2)
if HR < 60: CL += 12 # low arousal / fatigue
── Driver emotion (world state / Qwen vision) ──────────────────
if stressed: CL += 10 if tired: CL += 8
── Audio (BabyNet fast-path → AST fallback) ────────────────────
if crying | animal: CL += 25 if shouting: CL += 20
if rattle: CL += 10
── Child / pet (world.seats — no radar lag) ────────────────────
per seat: CL += 5 + distress×40 + HR_over×1.5 (cap 40)
── Road quality (IMU) ──────────────────────────────────────────
if pothole: CL += 18 if rough: CL += 8 if ahead<80m: +5
── Vision (Qwen + MediaPipe + YOLOv8n) ─────────────────────────
if drowsy: CL += 15 if loose_object: CL += 6–10
── Visibility / speed ──────────────────────────────────────────
if vis=low: CL += 12 if speed>100: CL += 8
return min(100, CL)
SCORE BANDS
0–25 Low · Nominal
26–55 Medium · Monitor
56–80 High · Advisory
81–100 Critical · Alert
KEY DESIGN CHOICES
→ Rule-based → full transparency, auditable
→ world.seats read directly → zero radar lag
→ HR deduplication across radar + world seats
→ Additive → drop-in ML scorer via same interface
→ Each factor independently traceable in HMI
→ Runs at 10 Hz, measured latency <1 ms

## Slide 5
FUSION ENGINE · MITIGATIONS
Confirm-First · Non-Intrusive · Rule-Driven
ADVISORY
Soothe Cabin
Crying/animal + child/pet seat → lower volume 30%, warm AC +1°C, soft lighting.
Calming Persona
Driver HR >95 or stressed → calm playlist, cool blue lighting, temp −1°C.
Alertness Boost
Driver HR <60 or tired → upbeat playlist, bright lighting, fresh-air burst.
Unsecured Item on Seat
Qwen detects object → advisory to stow before sudden braking.
Cabin Monitoring Active
Child/pet detected, no audio → radar vitals confirmed, adjustable.
WARNING
Seatbelt Not Engaged
Seat occupied but buckled=false → chime + visual. Fires immediately on configure.
Secure Before Road Hazard
Loose object + pothole <120 m → urgent secure advisory before impact.
Child / Pet HR Alert
Child HR >115 (pet >125) → warning. >threshold+20 → critical.
Passenger Distress
Shouting detected → check passenger, consider pulling over.
CRITICAL
CHILD PRESENCE ALERT
Child in rear, no driver → horn + lights + notification. No confirm required.
⚡ Grace Period 6s — confirmed/dismissed mitigations retained 6s after condition clears, preventing flicker from momentary sensor noise.

## Slide 6
SENSING STACK
Four Modalities · Privacy-Preserving · Graceful Degrade
📡 RADAR (MMWAVE)
→ 4-seat occupancy map
→ Contactless HR via Doppler
→ Respiration rate (rpm)
→ Micro-motion / agitation
→ Child-left-behind detection
→ Ref HW: TI IWR6843 / AWR
🎙️ AUDIO
→ BabyNet CNN — mel-spec, ~10ms GPU
→ Classes: none/crying/talking/happy
→ ≥0.60 conf → fast-path bypass
→ AST fallback — 527-class AudioSet
→ Detects: crying, barking, rattle
→ Conf threshold: 0.25 (bus topic)
📷 VISION
→ Qwen2-VL-2B — per-seat JSON
→ kind + emotion + buckled + objects
→ MediaPipe — EAR drowsiness
→ YOLOv8n — loose COCO objects
→ Priority: Qwen > MediaPipe > YOLO
→ Vision override guard on manual kinds
📳 IMU + VEHICLE
→ Road quality: smooth/rough/pothole
→ Pothole-ahead distance (m)
→ Speed (km/h) from CAN bus
→ Visibility: good/low/fog/rain
→ Pre-emptive object-securing trigger
→ Corroborates audio / radar events
Sensor priority chain: Radar occupancy → World state override → Qwen vision → MediaPipe | BabyNet fast-path → AST fallback | All nodes publish independently — fusion never blocked.

## Slide 7
AI MODELS
On-Device · No Cloud · Packaged in models/
Qwen2-VL-2B-Instruct
Qwen/Qwen2-VL-2B-Instruct
Vision-language model analyzing each camera frame. Returns structured JSON per seat: occupant kind, emotion, buckled state, and loose objects list.
4-bit NF4 quant
~2.5 GB VRAM
100–150 ms/frame
RTX 3080
BabyNet CNN
models/baby_net.pt
Custom mel-spectrogram CNN trained on baby audio samples. Fast-path classifier. Falls back to AST when confidence < 0.60.
Custom trained
~458 KB
~10 ms GPU
4 classes
AST — AudioSet
MIT/ast-finetuned-audioset-10-10-0.4593
Audio Spectrogram Transformer fine-tuned on 527-class AudioSet. AST fallback for BabyNet low-confidence. Detects crying, barking, rattle, speech.
527 AudioSet classes
~330 MB
thresh 0.15
CPU inference
MediaPipe FaceLandmarker
models/face_landmarker.task
478 facial landmarks → EAR drowsiness + heuristic emotion from mouth/eye geometry. Runs as fallback when Qwen is absent.
float16
3.6 MB
EAR thresh 0.20
Real-time
YOLOv8n
models/yolov8n.pt
Nano YOLO for fast object detection. Identifies loose objects in cabin (bag, bottle, laptop). Triggers secure-object pothole advisory.
COCO 80 classes
6.3 MB
~10 ms
conf 0.35
MODEL STRATEGY
→ All 5 models packaged in models/ — fully offline
→ Qwen overrides MediaPipe/YOLO when available
→ BabyNet fast-path → AST cascade on low confidence
→ Vision override guard — manual seat config protected
→ download_models.py for one-shot packaging

## Slide 8
DEMO SCENARIOS
7 Scripted Situations · All Verified End-to-End
#
Scenario
Sensors Triggered
CL Score
Mitigation Fired
1
Idle
All baseline
~5 Low
None
2
Baby Crying
Audio (crying) + Radar (child seat)
~35 Medium
Soothe Cabin
3
Driver Stress
Radar (HR↑, RESP↑) + Vision (emotion)
~42 Medium
Calming Persona
4
Pothole Ahead
IMU (pothole_ahead_m) + Object on seat
~58 High
Secure Before Road Hazard
5
Seatbelt Off
World state (buckled=false)
+12 Medium
Seatbelt Not Engaged
6
Child Left Behind
Radar (child rear, no driver)
~70 Critical
CHILD PRESENCE ALERT
7
Night Drive
Vehicle (low visibility + speed >100)
~65 High
Alertness Boost + Visibility
Confirm-First on all advisories | Immediate on safety-critical (seatbelt, child-left) | 6s grace period on dismiss

## Slide 9
TECHNICAL STACK
Backend · Frontend · Communication · Models
BACKEND — PYTHON 3.11
→ FastAPI + uvicorn — WebSocket /ws + REST
→ bus.py — async pub/sub, bounded queue, <1ms
→ world.py — shared ground-truth cabin state
→ fusion.py — 10Hz loop, rule-based scorer
→ sensors/ — 6 independent async nodes
→ scenarios.py — scripted demo world mutations
FRONTEND — REACT 18
→ CDN-free local libs (Babel 7.12.17 pinned)
→ SensorView: Video, Audio, Radar, IMU, Seat widgets
→ InfotainmentView: Gauge, Mitigation cards, Scenarios
→ TimelineBar: Manual / Live A/V / Scenario mode
→ RadarWidget: kind selector + HR sliders per seat
→ No polling — WebSocket push at 10Hz
COMMUNICATION PROTOCOL
→ WebSocket /ws — bidirectional JSON
→ FE→BE: audio_chunk, vision_frame, configure_seat
→ FE→BE: scenario, confirm, dismiss commands
→ BE→FE: full fused state per tick (10Hz)
→ audio_chunk: Float32 array, 0.96s @ 16kHz
→ vision_frame: base64 JPEG from webcam
KEY INVARIANTS
→ Sensor nodes never block — each has its own Hz
→ Swap node body only to go to real hardware
→ ML scorer can replace rule engine, same interface
→ Fusion reads world.seats directly — no stale radar
→ HR deduplication across world + radar sources
→ Grace period prevents flicker on sensor noise

## Slide 10
INNOVATION & SCORING
Why CabinSense Wins on Every Dimension
🎯 INNOVATION
→ Radar contactless vitals as cognitive-load signal
→ One fusion engine for all 5 use cases
→ Pre-emptive object-securing before pothole
→ Qwen2-VL per-seat: kind + emotion + objects
→ Custom BabyNet CNN fast-path classifier
🧑‍✈️ DRIVER-CENTRIC
→ Confirm-first on every mitigation
→ 6s grace period — no flicker from noise
→ Mode system clearly shown in HMI
→ Safety-critical bypasses confirm immediately
→ Optimistic UI — instant feedback on config
✅ FEASIBILITY
→ Reuses existing / near-term cabin sensors
→ SDV-aligned async bus topology
→ <1ms fusion latency, 10Hz rate
→ Fully offline — no cloud dependency
→ Swap node body only for real hardware
🛡️ SAFETY
→ Child / pet welfare: vitals + HR alerts
→ Child-left-behind: immediate critical (no confirm)
→ Seatbelt misuse: real-time, fires on configure
→ Pre-emptive pothole + loose-object hazard
→ Driver fatigue multimodal corroboration
💼 BUSINESS VALUE
→ Premium / EV cabin refinement differentiator
→ ADAS expansion into internal cabin awareness
→ Upgradeable SDV feature via software update
→ Privacy-preserving radar — no GDPR concerns
→ One platform, 5 revenue use cases
📡 RADAR DIFFERENTIATOR
→ Production-relevant: TI IWR6843 / AWR class
→ Privacy-preserving: no camera for sensitive data
→ Only sensor giving contactless driver vitals
→ Direct cognitive-load signal (HR, resp, motion)
→ Child-left detection even when camera is off

## Slide 11
CabinSense
The cabin is the last unmonitored space in a connected vehicle.
CabinSense closes that gap.
<1ms
Fusion Latency
5
Models On-Device
10
Mitigations
10Hz
Fusion Rate
Multi-Modal Fusion
Radar Vitals
Confirm-First UX
Child Safety
Fully Offline
SDV-Ready
github.com/PrashantKramadhari/in-cabin-hackthon